## Slide 1
AgroSense
An IoT-Based Smart Farming and Crop Monitoring System
Final-DEFENSE PRESENTATION • B.Sc. ENGINEERING IN CSE
Md Emam Masum
ID: 220201056
Zihan Hossain
ID: 220201067
Supervised by: Taher Muhammad Mahdee
Associate Professor
Co-Supervised by: Mahadi Hasan
Assistant Professor
Department of Computer Science and Engineering (CSE)
Bangladesh Army University of Science & Technology (BAUST)
August 2026

## Slide 2
OUTLINE
What We'll Cover
01
Introduction
02
Related Works
03
Problem Statement
04
Objectives
05
Proposed Methodology
06
Dataset
07
Project Timeline
08
Results
09
Expected Outcomes
10
Team Roles & Contributions
11
Conclusion
12
References
AgroSense — IoT Smart Farming & Crop Monitoring System
2 / 25

## Slide 3
INTRODUCTION
Introducing AgroSense
Agriculture in regions like Bangladesh still relies on manual, guesswork-driven irrigation. AgroSense brings a low-cost IoT sensor node together with a real-time cloud dashboard to close that gap.
🌾
Domain & Relevance
IoT-based smart farming pairs low-cost sensors, cloud databases, and automation to replace manual, guesswork-driven irrigation practices.
🚜
Application Area
Small and mid-scale farms that need remote soil, water, and climate monitoring with pump control accessible from any phone or browser.
AgroSense — IoT Smart Farming & Crop Monitoring System
3 / 25

## Slide 4
RELATED WORKS
Related Works & Existing Solutions
🏭
Commercial Precision-Ag Platforms
Full-featured systems (e.g. Netafim, CropX) give accurate monitoring but are too costly for small farms.
🔧
DIY / Open-Source IoT Sensors
Community ESP32/Arduino projects read soil data but usually lack a cloud dashboard or automated control.
📄
Academic IoT-Irrigation Studies
Prior research shows soil-moisture-based irrigation, often as lab prototypes without a full web interface.
📱
Mobile Farm-Monitoring Apps
Existing apps visualize sensor data but rely on manual entry or lack real-time automated pump logic.
AgroSense — IoT Smart Farming & Crop Monitoring System
4 / 25

## Slide 5
PROBLEM STATEMENT
The Challenge in Modern Agriculture
💧
Water Waste
Manual irrigation wastes up to 40% more water than needed.
📊
No Live Data
Farmers can't see soil, temperature, or crop conditions remotely.
🌧️
Weather Blind
Rain and water-level changes go undetected.
💡
No Automation
Pump control is entirely manual, no threshold logic.
💸
High Cost
Commercial precision-ag platforms are unaffordable.
🔌
No Integration
Sensors, cloud data, and irrigation control are disconnected.
AgroSense — IoT Smart Farming & Crop Monitoring System
5 / 25

## Slide 6
OBJECTIVES
Project Objectives
🌱
01
Multi-Sensor IoT Node
Design and deploy an ESP32-based node with 7 sensors: soil moisture, rain, water level, light, soil & air temperature, and humidity.
☁️
02
Real-Time Cloud Dashboard
Develop a 9-page, mobile-responsive web dashboard synced with Firebase Realtime Database every 2 seconds.
⚡
03
Automated Pump Control
Implement threshold-and-hysteresis auto-irrigation with manual override to cut water waste and manual labor.
AgroSense — IoT Smart Farming & Crop Monitoring System
6 / 25

## Slide 7
PROPOSED METHODOLOGY
System Workflow — Sense, Send, Store, Serve, Act
🌱
Field Sensing
ESP32 reads 7 sensors
every 2 seconds
1
📡
Firmware Processing
Calibrate ADC values,
compute % readings
2
☁️
Cloud Sync
Push to Firebase
/latestReading + /history
3
📊
Web Dashboard
9-page PWA renders
live data & charts
4
⚡
Decision Logic
Threshold + hysteresis
auto-irrigation check
5
Closed-Loop Automation
When soil moisture falls below the threshold − hysteresis band, the ESP32 activates the relay to run the pump; when it rises above threshold + hysteresis, the pump stops. A manual override from the dashboard can take precedence at any stage, and this decision instantly updates the cloud state, which reflects back on the dashboard in real time.
AgroSense — IoT Smart Farming & Crop Monitoring System
7 / 25

## Slide 8
WEB DASHBOARD
Main Dashboard
🔐 Login Page
AgroSense — IoT Smart Farming & Crop Monitoring System
8 / 25

## Slide 9
WEB DASHBOARD
Live Monitoring, Pump Control & Sensors
📡 Live Monitoring
💧 Pump Control
🔬 Sensors
AgroSense — IoT Smart Farming & Crop Monitoring System
9 / 25

## Slide 10
WEB DASHBOARD
History, Charts, Reports, Settings & Account
📋 History
📈 Charts
📄 Reports
⚙️ Settings
👤 Account Login
AgroSense — IoT Smart Farming & Crop Monitoring System
10 / 25

## Slide 11
SYSTEM DESIGN
Three-Tier System Architecture
Sensor node (ESP32) → Firebase Cloud (RTDB, Auth, Hosting) → Web Dashboard, showing the full data path end to end.
AgroSense — IoT Smart Farming & Crop Monitoring System
11 / 25

## Slide 12
HARDWARE
Complete Wiring Diagram
ESP32 DevKit V1 wired to all 7 sensors, the OLED display, and the relay-driven pump circuit.
AgroSense — IoT Smart Farming & Crop Monitoring System
12 / 25

## Slide 13
DATABASE DESIGN
Firebase Realtime Database — Data Model
Entity-relationship view of the RTDB schema: latestReading, history, config, and alerts nodes.
AgroSense — IoT Smart Farming & Crop Monitoring System
13 / 25

## Slide 14
SYSTEM DIAGRAMS
Level-0 Data Flow Diagram (DFD)
How sensor data moves between the ESP32 node, cloud database, and the farmer/user.
AgroSense — IoT Smart Farming & Crop Monitoring System
14 / 25

## Slide 15
SYSTEM DIAGRAMS
Sequence Diagram — Automated Irrigation Cycle
Step-by-step message flow between sensor, ESP32, Firebase, and dashboard during one irrigation cycle.
AgroSense — IoT Smart Farming & Crop Monitoring System
15 / 25

## Slide 16
SYSTEM DIAGRAMS
Actors (farmer, ESP32 device) and the core use cases the AgroSense platform supports.
AgroSense — IoT Smart Farming & Crop Monitoring System
16 / 25
Development Schedule — 8-Week Gantt Chart

## Slide 17
PROJECT MANAGEMENT
Detailed task-level Gantt chart complementing the milestone timeline shown earlier.
AgroSense — IoT Smart Farming & Crop Monitoring System
17 / 25
Use-Case Diagram

## Slide 18
DATASET
Sensor Data Collected
Parameter | Sensor | GPIO Pin | Range / Output
Soil Moisture | Capacitive (ADC1) | GPIO34 | 0–100%
Rain Level | Analog wetness (ADC1) | GPIO35 | 0–100%
Water Level | Reservoir analog (ADC1) | GPIO33 | 0–100%
Light Intensity | LDR (ADC1) | GPIO32 | ADC lux value
Soil Temperature | DS18B20 (1-Wire) | GPIO27 | °C
Air Temp & Humidity | DHT11 (digital) | GPIO4 | °C / %RH
AgroSense — IoT Smart Farming & Crop Monitoring System
18 / 25
Data is streamed live via ESP32 firmware, pushed to Firebase every 2 seconds, and logged in /history for charting and reports.

## Slide 19
PROJECT / THESIS TIMELINE
8-Week Development Schedule
W1
Requirement Analysis & Literature Review
W2
Hardware Procurement & Circuit Design
W3
Firmware Development (Sensors + Wi-Fi)
W4
Firebase Schema & Cloud Integration
W5
Web Dashboard — Core Pages
W6
Pump Control & Automation Logic
W7
Testing (17 Test Cases) & Debugging
W8
Documentation & Pre-Defense Prep
AgroSense — IoT Smart Farming & Crop Monitoring System
19 / 25

## Slide 20
PRELIMINARY RESULTS / PROGRESS
Where We Stand Today
7
Sensors integrated
2s
Live update rate
9
Dashboard pages built
17/17
Test cases passed
Firmware complete: reads all 7 sensors, drives OLED display, uploads to Firebase every 2 seconds.
Web dashboard functional across Login, Live Monitoring, Pump Control, Charts, History, and Reports pages.
Threshold + hysteresis (±5%) auto-irrigation logic validated with manual override support.
Field-style testing completed: all 17 test cases passed, covering sensors, automation, Wi-Fi recovery, and auth.
AgroSense — IoT Smart Farming & Crop Monitoring System
20 / 25

## Slide 21
EXPECTED OUTCOMES
What AgroSense Will Deliver
💧
Reduced Water Waste
Threshold-based auto-irrigation cuts unnecessary watering compared to manual routines.
📲
Remote Visibility
Farmers monitor soil, water, and climate conditions live from any phone or browser.
⚙️
Reliable Automation
Hysteresis logic and manual override prevent pump stress and give the farmer final control.
💰
Affordable Precision Agriculture
A low-cost ESP32 + Firebase stack brings capabilities of costly commercial platforms within reach.
AgroSense — IoT Smart Farming & Crop Monitoring System
21 / 25

## Slide 22
TEAM ROLES & CONTRIBUTIONS
Team Roles & Contributions
Taher Muhammad Mahdee
Supervisor
Associate Professor, Dept. of CSE (BAUST)
Mahadi Hasan
Co-Supervisor
Assistant Professor, Dept. of CSE (BAUST)
Md Emam Masum
ID: 220201056
Software Back-end, Database & Deployment, Hardware Integration, Firmware & Hardware Testing.
Zihan Hossain
ID: 220201067
Software Front-end, Hardware Collection,
Diagrams & Documentations, overall UI design, Software Testing.
AgroSense — IoT Smart Farming & Crop Monitoring System
22 / 25

## Slide 23
CONCLUSION
Conclusion
1
AgroSense addresses four core problems in manual irrigation — water waste, blind monitoring, weather risk, and high commercial cost — with one integrated IoT platform.
2
All three objectives were met: a 7-sensor ESP32 node, a real-time Firebase-synced dashboard, and automated threshold-hysteresis pump control.
3
The system was validated with 17/17 test cases passed during field-style testing, confirming its accuracy and reliability.
4
AgroSense proves that affordable, integrated IoT can bring precision agriculture within reach of small-scale farmers.
AgroSense — IoT Smart Farming & Crop Monitoring System
23 / 25

## Slide 24
REFERENCES
References
IEEE format — literature-review and technical reference list
[1] S. Rahman and T. Islam, “IoT-Based Smart Irrigation Systems: A Review of Architectures and Applications,” Int. J. Computer Applications, vol. 186, no. 4, pp. 12–19, 2024.
[2] M. Chowdhury and N. Akter, “Design of a Low-Cost Sensor Network for Precision Agriculture in Developing Regions,” Proc. Int. Conf. on Innovation in Engineering and Technology, pp. 1–6, 2023.
[3] R. Karim, “Cloud-Based Real-Time Data Logging for Embedded IoT Applications,” J. Emerging Technologies in Computing, vol. 9, no. 2, pp. 45–53, 2022.
[4] Espressif Systems, ESP32 Technical Reference Manual, Version 5.1, Shanghai: Espressif Systems, 2023.
[5] Google LLC, Firebase Realtime Database Documentation, 2024. [Online]. Available: firebase.google.com/docs/database.
AgroSense — IoT Smart Farming & Crop Monitoring System
24 / 25

## Slide 25
🌱
Thank You
AgroSense — IoT-Based Smart Farming & Crop Monitoring System
Md Emam Masum (220201056) • Zihan Hossain (220201067)
Supervised by: Taher Muhammad Mahdee (Associate Professor) • Co-Supervised by: Mahadi Hasan (Assistant Professor)
Department of CSE • Bangladesh Army University of Science & Technology (BAUST) • August 2026
🌐 smart-farming-3d1f2.web.app